## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, Idea, VODAFONE & Reliance JIO (FDD/TDD) LTE

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 404
MNC | 97
APN | Jionet
Operator | Airtel 4G
MCC | 404
MNC | 56
APN | Airtelgprs.com
Operator | VI
MCC | 404
MNC | 56
APN | www
Operator | BSNL
MCC | 404
MNC | 54
APN | bsnlnet

## Slide 3: Operator Information 1
Functionality | Airtel
Website: http://www.airtel.com/ WAP APN: airtelgprs.com | 
Customer care | 199
MNC | 56
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800,850 MHz – FDD(Band 3)
USSD | To check MDN: *282#
 | Balance check: *123#
 | Data Balance check: *121*114#
VoLTE | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 97
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: http://www.myvi.in WAP APN: WWW | 
Customer care | 198
MNC | 56
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40,41)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN*199#
 | Balance check198
 | Data Balance check: 121
VoLTE | Supported
CSFB | Supported to 2G / 3G

## Slide 6: Operator Information 4
Functionality | BSNL
Website: http://portal.bsnl.in WAP APN: bsnlnet | 
Customer care | 1503
MNC | 54
Bands supported | Both FDD and TDD
 | GSM 2G 900 – B - PGSM
 | UMTS 3G 2100 – B - U1[5]
USSD | To check No.-*222#
 | Main Balance check-*123*1#
 | 2G&3G Data Balance check- *123*5#
VoLTE | Not Supported
CSFB | Not Supported

## Slide 7: Drive Route
Near Cell :- Stationary: RSRP : -65dbm to -75dbm
Cell Edge :- Stationary: RSRP : -95dbm to -110dbm
Mixed :- Mobility: RSRP : -65dbm to -110dbm

## Slide 8: Near Cell (Airtel)
Near cell(NC) | longitude | latitude | RSRP | Cell id | FDD E-ARFCN
1 | 77.735940 | 28.967399 | -70 | 43 | 1276
RSRP:
-65dbm to 75dbm
Garh road near Hotel Broadway inn, mangal Pandey Nagar ,Meerut.

## Slide 9: Edge Cell (Airtel)
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.727405 | 28.948001 | -107 | 51 | 40140
RSRP:
-95dbm to -110dbm
Shastri Nagar, L Block, Meerut

## Slide 10
Mixed Mobility:- University road ,Meerut, U.P
RSRP: -65dbm to -110dbm
University road ,Meerut, U.P

## Slide 11
Airtel Band HO
Band Hand Over | longitude | Latitude | RSRP
1 | 77.717114 | 28.961156 | -85 to 105 dBM

## Slide 12: Near Cell (Reliance JIO)
Near cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.727036 | 28.993797 | -66 | 22 | 39150
RSRP:
-65dbm to -75dbm
CCS university road ,Pulse of market, Meerut, U.P

## Slide 13
Edge Cell (Reliance JIO)
Edge cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.727036 | 28.993797 | -98 | 20 | 39150
RSRP:
-95dbm to -110dbm
Cant, CMO office, Civil Lines , Meerut, U.P

## Slide 14
Mixed Mobility:-Cant Meerut , U.P
RSRP: -65dbm to -110dbm

## Slide 15: Inter Band Handover (FDD-TDD), JIO 4G
Band Handover | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 77.727036 | 28.993797 | -85 | 288 | 39348

## Slide 16: RJIO Band 40 Near Cell:
CCS university road ,Pulse of market, Meerut, U.P

## Slide 17: RJIO Band 40 Edge Cell:
Cant, CMO office, Civil Lines , Meerut, U.P

## Slide 18: Near Cell VI:
Near cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.730666 | 28.941436 | -68 | 23 | 1276
Police line road Meerut , U.P
RSRP:
-65dbm to -75dbm

## Slide 19: Edge Cell VI:
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.728051 | 28.946611 | -104 | 32 | 215
RSRP:
-95dbm to -110dbm
Shastri Nagar ,L Block, Meerut U.P

## Slide 20: Mixed coverage area Vodafone:
RSRP: -65dbm to -110dbm
Shastri Nagar L-Block to
Police line road Meerut , U.P

## Slide 21
VI SRVCC to HSPA:

## Slide 22: Vi Band 3<>8<>41 Handover

## Slide 23: G net Tracker Drive Route

## Slide 24: Google drive route-

## Slide 25: THANK YOU
MARQUIS TECHNOLOGIES