## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, VI& Reliance JIO ,BSNL(FDD/TDD) LTE

## Slide 2: Dehradun/India
S. No. | Operator |  | Supported Bands | Supported Features by Network
1 | Major | Airtel | LTE FDD B5 & TDD B40/N78 | VoWiFi/VoLTE/4G/2G/5G NSA
2 |  | JIO | LTE FDD B3/B5& TDD B40/N78/N28 | VoWiFi/VoLTE/4G/5G SA
3 |  | VI | LTE FDD B3,B8 TDD-B40 | VoWiFi/VoLTE/4G/2G
4 | Minor | BSNL | UTMS2100/1800 ,GSM 1800/900MHZ & LTE-2100MHz | 3G/2G/4G
Operator Details:

## Slide 3: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 870
APN | Jionet
Operator | Airtel 4G
MCC | 404
MNC | 97
APN | Airtelgprs.com
Operator | VI
MCC | 404
MNC | 56
APN | Internet
Operator | BSNL
MCC | 404
MNC | 54
APN | bsnlnet

## Slide 4: Operator Information 1
Functionality | Airtel
Website: http://www.airtel.com/ WAP APN: airtelgprs.com | 
Customer care | 199
MNC | 97
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800,850 MHz – FDD(Band 3)
USSD | To check MDN: *282#
 | Balance check: *123#
 | Data Balance check: *121*114#
VoLTE | Supported
CSFB | Supported (CSFB to 2G)

## Slide 5: Operator Information 2
Functionality | RELIANCE JIO
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 870
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
CSFB | Not Supported

## Slide 6: Operator Information 3
Functionality | VI
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 56
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40,41)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN*199#
 | Balance check198
 | Data Balance check: 121
VoLTE | Not supported
CSFB | NA

## Slide 7: Drive Route
Near Cell :- Stationary: RSRP : -65dbm to -75dbm
Cell Edge :- Stationary: RSRP : -95dbm to -110dbm
Mixed :- Mobility: RSRP : -65dbm to -110dbm

## Slide 8: Near Cell (Airtel)
Near cell(NC) | longitude | latitude | RSRP | Cell id | E-ARFCN
1 | 77.905095 | 30.30156 | -66 | 22 | 40140
RSRP:
-65dbm to 75dbm
DEV COLONY RATANPUR DEHRADUN

## Slide 9
5G Near Cell,Airtel
Lat/Long -30.3278452,78.047343
Specification –Stable Airtel 5G NSA network
Good Throughput

## Slide 10
NR to LTE Handover ,Airtel
Lat. 30.342522, 78.016255 Location –Near Forest Research Institute ,Chakratta Road Specification –Band Handover ,Weak coverage

## Slide 11
NR to LTE Handover ,JIO
Lat/Long 30.368942,78.0942517to
Lat/Long 30.3700158,78.0817204 Location – Dehradun to Mussoorie Diversion Road

## Slide 12: Edge Cell (Airtel)
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.901746 | 30.292958 | -115 | 4 | 1526
RSRP:
--100 - -115
KADWAPANI ,MALAN DEHRADUN

## Slide 13
Mixed Mobility:- Airtel (Dehradun )
RSRP: -60dbm to -110dbm

## Slide 14
DRIVE ROUTE Airtel 5G (Dehradun) Specification-Call/Handover/Cell Reselection/Redirection

## Slide 15
Airtel Band HO
Band 1<>3<>40 Handover

## Slide 16
MATT Tool InterBand Handover Results for Airtel

## Slide 17: Near Cell (Reliance JIO)
Near cell(NC) | longitude | latitude | RSRP | Cell id | E-ARFCN
1 | 77.907138 | 30.303688 | -60 | 49 | 2484
RSRP:
-57dbm to -75dbm
Ratanpur chok Dehradun

## Slide 18: 5G Near Cell JIO ,Dehradun
Lat/Long. 30.3153536,78.0355921 Location – Near Prince Chowk ,Dehradun Specification –VONR & 5G STABLE NETWORK

## Slide 19
Edge Cell (Reliance JIO)
Edge cell(NC) | longitude | latitude | RSRP | Cell id | E-ARFCN
1 | 77.902301 | 30.292675 | -114 | 4 | 1526
Malan Dehradun
RSRP:
-95dbm to -110dbm

## Slide 20
Mixed Mobility:- JI0 RATANPUR Dehradun
RSRP: -60dbm to -110dbm

## Slide 21: Inter Band Handover (FDD-TDD), JIO 4G

## Slide 22: MATT Tool InterBand Handover Results for Jio

## Slide 23: RJIO Band 40 Near Cell:
RSRP Range for Near Cell :
-65dbm to -75dbm
RATANPUR CHOK DEHRADUN

## Slide 24
DRIVE ROUTE JIO 5G (Dehradun) Specification-Call/Handover/Cell Reselection/Redirection

## Slide 25: Near Cell VI:
Near cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 77.907303 | 30.301573 | -66 | 22 | 1276
ADARSH COLONY RATANPUR DEHRADUN
RSRP:
-65dbm to -75dbm

## Slide 26: Cell Edge VI:
Edge cell(EC) | longitude | latitude | RSRP | Cell id | E-ARFCN
1 | 77.906050 | 30.295543 | -109 | 33 | 215
RSRP:
-95dbm to -105dbm
KARBARI GRANT DEHRADUN

## Slide 27: Mixed coverage area Vodafone:

## Slide 28: VIBand 1<>3<>8 Handover

## Slide 29
SRVCC for VI operator
Lat/Long 30.368942,78.0942517to
Lat/Long 30.216554, 78.122021 Location – Dehradun to Haridwar Road

## Slide 30
DRIVE ROUTE Vi 4G (Dehradun) Specification-Call/Handover/Cell Reselection/Redirection

## Slide 31: MATT Tool InterBand Handover Results for VI

## Slide 32: G net Tracker Drive Route

## Slide 33
Drive Route

## Slide 34: THANK YOU
MARQUIS TECHNOLOGIES