## Slide 1: MARQUIS TECHNOLOGIES
Drive Route – Kolkata(India)

## Slide 2
Kolkata
Country | India
Continent | Asia
State | West Bengal
City | Kolkata
Time Zone | GMT + 5:30
International Dialling Code | +91

## Slide 3
Operator Information
Operator | RAT (DRX) |  |  | Band(MHZ) | LTE Band | Infra
 | 2G | 3G | LTE |  |  | 
Airtel | 470 | 640 | 1280 | 1800 /2300 | Band 3, 8 & 40 | Ericsson
Vodafone | 705 | 640 | 1280 | 1800/2500 | Band 1, 3 & 41 | Huawei & NSN
JIO | -- | -- | 1280 | 850/1800/2300 | Band 3, 5 & 40 | Samsung
Idea | 705 | 640 | 1280 | 2100/2500 | Band 1, 3 & 41 | Huawei & NSN

## Slide 4
Operator Information
Operator | JIO-4G | Airtel-4G | Vodafone 4G | Idea
MCC | 405 | 404 | 404 | 405
MNC | 873 | 31 | 30 | 848
APN | Jionet | airtelgprs.com | www | internet
Manual APN Settings for JIO, Airtel & Vodafone in Kolkata (India)

## Slide 5
Additional Information
MMS is not supported by RJIO, Airtel 4G & Airtel Volte.
Airtel, Vodafone and IDEA Supporting IMS and Vowifi services.
In Vodafone MMS is supported in 4G/VoLTE as well.
Idea 4G supports MMS
Airtel, Vodafone and IDEA 3G not available in Kolkata.

## Slide 6
RSRP Criteria
Near Cell :-Stationary: RSRP : -55dbm to -85dbm
Cell Edge :-Stationary: RSRP : -95dbm to -115dbm
Mixed :-Mobility: RSRP : -55dbm to -120dbm

## Slide 7
Drive Route_Kolkata
Operator: Jio LTE VoLTE
Mode: Idle & Connected

## Slide 8: JIO 4G band Reselection (Band 40 to band3 to band 5) Route: New Town Area

## Slide 9: JIO 4G band handover (band 40 band 3to band 40) Route: New Town Area

## Slide 10: Edge cell area For jio 4G

## Slide 11: Find a Band switch area testing for JIO 4G(band 40 to 5 to 40)

## Slide 12: Medium signal strength testing for Jio 4G

## Slide 13: NON CA Cell to CA Cell Handover LOCATION : HATISALA BUSSTAND to WELFIT TALAX

## Slide 14: Between High Building

## Slide 15: CA Cell to CA Cell IDLE HandOver LOCATION : WELFIT TALAX

## Slide 16: CA Cell to non CA Cell IDLE Handover LOCATION : HATISALA BUSSTAND to WELFIT TALAX

## Slide 17: Medium signal strength testing for Jio 4G

## Slide 18: RJIO Band 40 Near Cell

## Slide 19: RJIO Band 40 Edge Cell
RSRP:-100 dbm to -110dbm
Longitude:22.561326
Latitude: 88.347947
Landmark:
Mayo road
4

## Slide 20: RJIO Band-5 Near Cell
Longitude: 88°29'29.18"E
Latitude: 88°29'29.18"E
Landmark: Ecospace

## Slide 21: RJIO Band-5 Edge Cell

## Slide 22: RJIO Band 3 Near Cell

## Slide 23: RJIO Band 3 Edge Cell

## Slide 24
Drive Route_Kolkata
Operator: Airtel LTE VoLTE
Mode: Idle & Connected

## Slide 25: Reselection from Band 3 to B40 to B3 Location: Uniworld to Unitech Gate 2

## Slide 26
Reselection from non CA cell to CA cell for Airtel operator
Location : Kalitala Road to Binayal Hall

## Slide 27
Reselection from CA cell to non CA cell for Airtel operator
Route : Nandan Kanan to shantipali

## Slide 28
Handover from CA cell to CA cell for Airtel operator
Route: Science City

## Slide 29: WEB PAGE LOADING AND APPS USING IN AREA OF HIGH DENSITY OF CROWD AND TALL BULIDINGS(Airtel 4G)

## Slide 30: Handover from Band 40 to B3 to B40 (During Call) Location: Chaturmas vyuastha samity to Hatisala

## Slide 31: Airtel 4G band handover (band3 to 40to 3)

## Slide 32: Handover from CA cell to Non-CA cell Location: Chaturmas vyuastha samity to Shapoorji circle

## Slide 33: Good signal strength for testing For Airtel 4G

## Slide 34: Medium signal strength for testing

## Slide 35: Edge cell area for testing For Airtel 4G

## Slide 36: Band switch area for testing

## Slide 37: Near Cell : Airtel Band 3 Science city, kolkata, west Bengal
RSRP: -65dbm to -75dbm
LAT & LONG: 22.531467,88.395553

## Slide 38: Edge cell:- Airtel Band 3 Golf green, kolkata, west Bengal
RSRP: -95dbm to -110dbm
LAT & LONG: 22.491869,88.361709

## Slide 39: Near Cell : Airtel Band 40 Ruby, kolkata, west Bengal

## Slide 40: Edge Cell : Airtel Band 40 Metro cash & Carry, kolkata, west Bengal

## Slide 41: Near Cell : Airtel Band 8 Kalikapur Bus stand, kolkata, west Bengal

## Slide 42: Edge Cell : Airtel Band 8 Young horizon School, kolkata, west Bengal

## Slide 43: Airtel 4G band handover (band40 to 8 to 40)

## Slide 44
Drive Route_Kolkata
Operator: Vodafone LTE VoLTE
Mode: Idle & Connected

## Slide 45: Reselection from Band 3 to B41 to B3 Location: Metro cash and carry to Science city

## Slide 46: Band Handover from Band 3 to Band 41 Location: Safuipara IOC petrol pump to GARFA

## Slide 47: Band Handover During call Location: Safuipara IOC petrol pump to GARFA

## Slide 48: Band handover from Band 41 to B1 to B41

## Slide 49: CA to non CA for Vodafone Location: Technopolis to central power research institute

## Slide 50: NON CA TO CA CELL VODAFONE Location: green wood nock to Safuipara IOC petrol pump

## Slide 51: CA cell to CA cell Vodafone Location: Green wood nock to Garfa

## Slide 52: SRVCC to 3G/2G,Baruipur Area

## Slide 53: SRVCC to 3G Location: Peyarabagan park to golf green post office

## Slide 54: SRVCC to 2G Location: Peyarabagan park to golf green post office

## Slide 55: IRAT from LTE to W Location: Basanti Hwy

## Slide 56: IRAT from LTE to W to G Location: Basanti Hwy

## Slide 57: Good signal strength for testing For Vodafone 4G

## Slide 58: Edge cell area for testing For Vodafone 4G

## Slide 59: Band switch area for testing for Vodafone

## Slide 60: Between High Rise building

## Slide 61: Near Cell : Vodafone Band 41 Science city, kolkata, west Bengal
RSRP: -65dbm to -75dbm
LAT & LONG: 22.531467,88.395553

## Slide 62: Edge Cell : Vodafone Band 41

## Slide 63: Near Cell : Vodafone Band 3

## Slide 64: Edge cell:- Vodafone Band 3 Golf green, kolkata, west Bengal
RSRP: -95dbm to -110dbm
LAT & LONG: 22.491869,88.361709

## Slide 65: Near Cell:- Vodafone Band 1 Bengal Chemical, kolkata, west Bengal

## Slide 66: Edge Cell:- Vodafone Band 1 Saltlake Stadium, kolkata, west Bengal

## Slide 67: Near Cell : Vodafone (Band L1) Das Para,Mukandapur, kolkata, west Bengal
Daspara, Mukandapur
Lat : 22.489666
Long : 88.413138

## Slide 68: IRAT Handover (Vodafone)
Basanti Highway
4G to 2G to 4G
Lat : 22.5243728
Long : 88.4345696

## Slide 69
Drive Route_Kolkata
Operator: Idea LTE/WCDMA/GSM
Mode: Idle & Connected

## Slide 70: Near Cell : Idea LTE Band 3 Science city, kolkata, west Bengal
RSRP: -65dbm to -75dbm
LAT & LONG: 22.531467,88.395553

## Slide 71: Edge Cell : Idea LTE Band 3,41 Baraipur, kolkata, west Bengal
LAT & LONG: 22.572645, 88.363892

## Slide 72: L2W IRAT : Idea Baraipur ,Kolkata
LAT & LONG: 22.572645, 88.363892

## Slide 73: W2G IRAT : Idea
LAT & LONG: 22.527062,88.441782

## Slide 74: IDEA SRVCC Route: Kalyanpur Road(Panchanantala Temple to Ramgopalpur Primary School)

## Slide 75: IDEA REDIRECTION (4G to 3G) Route: Basanti Highway(Science city to Koyla Dipo Bus Stand)

## Slide 76: IDEA Cell RESELECTION (4G to 3G) Route: Basanti Highway(Chowbaga bajar to bantala pumping station)

## Slide 77: IDEA Intra band Inter frequency for B3(1466-1441) Route: EM Bypass(Ruby to Metropolis)

## Slide 78: IDEA Band handover (B41 to B3 to B41) Route: EM Bypass(VIP Nagar to Dhapa)

## Slide 79: IDEA Band handover (B3 to B41 to B3) Route: EM Bypass(Mukundupur to Rajdanga)

## Slide 80: IDEA Band handover (B3 to B1 to B3 to B41) Route: EM Bypass(Panchanantala temple to Jisan Market)

## Slide 81: IDEA IRAT handover (4G to 2G to 4G to 3G) Route: Kalyanpur Road(Ramgopal primary School to Kalyanpur)

## Slide 82: Near Cell : IDEA (Band L41 & L3) Das Para,Mukandapur, kolkata, west Bengal
Daspara, Mukandapur
Lat : 22.489666
Long : 88.413138

## Slide 83: Edge Cell : IDEA (Band L41 & L3) Kalikapur, kolkata, west Bengal
Singhabari
Lat : 22.496485
Long : 88.398070

## Slide 84: IRAT Handover (Idea)
4G to 2G to 4G
Lat: 22.5662726
Long : 88.3979941
                Beleghata, Kolkata

## Slide 85: THANK YOU
MARQUIS TECHNOLOGIES
www.marquistech.com