## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, VI & Reliance JIO (FDD/TDD) LTE
Location : Bangalore

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 861
APN | jionet
Operator | Airtel 4G
MCC | 404
MNC | 45
APN | airtelgprs.com
Operator | VI
MCC | 404
MNC | 86
APN | internet
Operator | BSNL
MCC | 404
MNC | 71
APN | Bsnlnet

## Slide 3: Operator Information 1
Functionality | Airtel
Website: https://www.airtel.in/ WAP APN: airtelgprs.com | 
Customer care | 198
MNC | 45
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800 – FDD(Band 3) LTE 900 – FDD(Band 8) LTE 2100 – FDD (Band 1)
USSD | To check MDN: *282#
 | Balance check: *123#
 | To check all services: *121#
VoLTE | Supported
VoWiFi | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: https://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 861
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
VoWiFi | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: https://www.myvi.in WAP APN: internet | 
Customer care | 198
MNC | 86
Bands supported | FDD
 | LTE 900 MHz – (Band 8)
 | LTE 2100 MHz – (Band 1)
 | LTE 1800 MHz – (Band 3)
USSD | To check MSISDN :*199#
 | Recharge : *199*5#
 | Balance check : *199*2#
VoLTE | Supported
VoWiFi | Not Supported
CSFB | Supported (CSFB to 2G/3G)

## Slide 6: Drive Route
Near Cell : Stationary: RSRP : -65dbm to -75dbm
Edge Cell : Stationary: RSRP : -95dbm to -110dbm
Mixed : Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
Near cell | longitude | Latitude | RSRP (dbm)
1 | 13.068945305972239 | 77.78497641252783 | -71
RSRP Range for Near Cell :
-65dbm to -75dbm
Near Safal market,
Bangalore

## Slide 8: Edge Cell (Airtel)
Edge cell | longitude | latitude | RSRP (dbm)
1 | 13.053365634511652 | 77.76178095703837 7 | -102
RSRP Range for Edge Cell :
-95dbm to -110dbm
Near
Kattamanallur,
Bangalore

## Slide 9
Mixed Coverage Area for Airtel
Mugabala to Krishnarajapura,
Bangalore

## Slide 10
Airtel Inter Band HO
Band 8 BAND 40 BAND 3

## Slide 11: MATT Tool InterBand Handover Results for Airtel

## Slide 12: Near Cell (Reliance JIO)
RSRP Range for Near Cell : -65dbm to -75dbm
Near Safal Market, Bangalore
Near cell | longitude | Latitude | RSRP (dbm)
1 | 13.068945305972239 | 77.78497641252783 | -71

## Slide 13
Edge Cell (Reliance JIO)
RSRP Range for Edge Cell :
-95dbm to -110dbm
Near
Kattamanallur,
Bangalore
Edge cell | longitude | latitude | RSRP (dbm)
1 | 13.053365634511652 | 77.76178095703837 7 | -102

## Slide 14
Mixed Coverage Area for Reliance JIO
KHB Layout to Kajisonnanahalli,
Bangalore

## Slide 15: Inter Band Handover (FDD-TDD) for JIO 4G
Band 40 Band 5 Band 3

## Slide 16: MATT Tool InterBand Handover Results for Jio

## Slide 17: Near Cell for VI:
Near Safal Market,
Bangalore
RSRP Range for Near Cell :
-65dbm to -75dbm
Near cell | longitude | Latitude | RSRP (dbm)
1 | 13.068945305972239 | 77.78497641252783 | -71

## Slide 18: Edge Cell for VI:
RSRP Range for Edge Cell :
-95dbm to -110dbm
Edge cell | longitude | latitude | RSRP (dbm)
1 | 13.053365634511652 | 77.76178095703837 7 | -102
Near
Kattamanallur,
Bangalore

## Slide 19: Mixed Coverage Area for VI:
KHB Layout to Kajisonnanahalli,
Bangalore

## Slide 20: VI Band Handover
Band 1 Band 3 Band 8

## Slide 21: MATT Tool InterBand Handover Results for VI

## Slide 22: Drive Route

## Slide 23: THANK YOU
MARQUIS TECHNOLOGIES