## Slide 1: MARQUIS TECHNOLOGIES
5G Drive Route – Thailand

## Slide 2: Drive Route
Near Cell :-Stationary: RSRP: -65dbm to -90dbm
Mixed :-Mobility: RSRP : -75dbm to -100dbm
Cell Edge :-Stationary: RSRP : -95dbm to -120dbm

## Slide 3
Operator | Mobility Scenario | Location Tested | Longitude / Latitude
AIS | 4G-3G-4G HO SPOT | SV City Parking | 13.67208, 100.54382
 | SRVCC to 3G | SV City Parking | 13.67208, 100.54382
 | IRAT | SV City Parking | 13.67208, 100.54382
 | Good Coverage for Testing | Flash express rama 3 | 13.67474, 100.53830
 | Poor Coverage for testing | SV City, Parking | 13.67208, 100.54382
 | OOS Area | SV City Basement | 13.67208, 100.54382
TrueMoveH | SRVCC to 2G | Not supported /Location not Found | NA
 | SRVCC to 3G | SV City Parking | 13.67208, 100.54382
 | 4G-3G-4G HO SPOT | SV City Parking | 13.67208, 100.54382
 | IRAT | SV City Parking | 13.67208, 100.54382
 | Good Coverage for Testing | RN Building | 13.67622, 100.54481
 | Poor Coverage for testing | SV City Parking | 13.67208, 100.54382
 | OOS Area | SV City Basement | 13.67208, 100.54382
DTAC | SRVCC to 3G | SV City Parking | 13.67208, 100.54382
 | SRVCC to 2G | Not supported /Location not Found | 
 | 4G-3G-4G HO SPOT | SV City Parking | 13.67208, 100.54382
 | IRAT | SV City Parking | 13.67208, 100.54382
 | Good Coverage for Testing | PATEX Flagship Store Rama 3 | 13.67461, 100.54320
 | Poor Coverage for testing | SV City Parking | 13.67208, 100.54382
 | OOS Area | SV City Basement | 13.67208, 100.54382

## Slide 4
Services Supported by AIS VoLTE Operator
AIS 5G/4G/3G/2G | GSM-900MHz & 1800MHz, B1(2100 MHz), B3(1800MHz), NR41 (2600 MHz),
OPERATOR | Features /Services | Supported(yes/No)
AIS (Major) | Reselection | Yes
 | Redirection | Yes
 | MMS /SMS | Yes
 | Volte | Yes
 | vowifi | Yes
 | PS Handover | Yes

## Slide 5
Operator | PLMN | 5G Tested Locations | Longitude / Latitude | ENDC combination Tested
AIS | 520/03 | Siam Square One | 13.74517, 100.53382 | LTE Band 1 + NR 41
 |  | SV City Rama3 | 13.67208, 100.54382 | LTE Band 1 + NR 41
TrueMoveH | 520/04 | Siam Square One | 13.74517, 100.53382 | LTE Band 3 + NR 07
 |  | SV City Rama3 | 13.67208, 100.54382 | LTE Band 3 + NR 07
DTAC | 520/05 | 5G Not Tested Till Now |  | 
Major Thailand Operators : Locations for 5G /NR Field Test

## Slide 6: AIS 5G VoLTE Good Coverage Area Band L1,L3 AND L8 WITH NR 41 BAND Route >>Flash Express Rama3 >> MS Saim
L1 AND L8 BANDS WITH NR 41
L1 AND L3 BAND WITH NR 41

## Slide 7: AIS 5G and 4g VoLTE Mix Coverage Area Route >> Chatukchak >> Bang Khen Road
4g and 5g mixed coverage
5g coverage ends here
5g area

## Slide 8: AIS weak 5G VoLTE Coverage Area Band NR 41, LTE band L1,L3 AND L8 Route >> Bang sue Road >> Bang Khen
Weak 5g area AIS
5g coverage ends

## Slide 9: AIS 5G VoLTE operator CA to non CA HO (B3_CA NR 41 to 4G L8_Non CA) Route>>Chatukchak to Nonthaburi road
EC:2
5g to 4g handover
First handover point

## Slide 10: Band HO from B3 to B1 and B1 to B40 for DTAC VoLTE operator Route Rama 3 to Saim Road

## Slide 11: Band HO from B1 to B3 in NR41 region during ongoing MO call AIS Route>> MS Saim to Saim Paragon

## Slide 12: Band HO from B1 to B8 during ongoing MO call for AIS Saim to MS Saim

## Slide 13: SRVCC AIS 5G VoLTE to 4G Volte On Rama 3 Road

## Slide 14: SRVCC 4G TO 3G – Happens ( 4G to 2G Not Found Loaction) Near Rame 3 River Front

## Slide 15: HO from one CA (B1+B3 AND NR 41) cell to another CA cell for NR CELLS AIS 5G VoLTE operator Route>> SV City Rama 3 to Ms Saim Road

## Slide 16: TruemoveH 5G LTE BAND HANDOVER (B3 +B1) to Non CA B28 Route >>Ms Saim to River Front Road

## Slide 17: TrueMoveH 5G Volte Operator Band Handover (B1 – B41) Route >>Central Saim >>> Paya Thai

## Slide 18: DTAC 4G VoLTE Band Handover B1 to B40 Route >> SV City >> Samut Prakan

## Slide 19: TrueMoveH 5G Volte operator CA (B1+B3) to Non CA B41 Route >> Central world Road >> Paya Thai

## Slide 20: TrueMoveH 5G Volte operator CA to CA Handover(B1) to (B3) Route >>MS Saim to SV City Rama3

## Slide 21: TrueMoveH 5G to 4G Volte operator SRVCC Location Route >> Near River Front Rama3

## Slide 22: TRuemoveH 5G Volte operator 4G to 3G to 4G Handover ( 4G To 2G to 4G Location Not Found) Route >>MS Saim to SV City and River front area

## Slide 23: TrueMoveH 4G long calls SV City to Phaya Thai

## Slide 24: ICE 4G Volte operator 4G to 3G to 4G Handover Route >> SV City to Chatuchak

## Slide 25: THANK YOU
MARQUIS TECHNOLOGIES
www.marquistech.com