## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, Idea, VODAFONE & Reliance JIO (FDD/TDD) LTE

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 866
APN | Jionet
Operator | Airtel 4G
MCC | 405
MNC | 53
APN | Airtelgprs.com
Operator | VI
MCC | 405
MNC | 753
APN | www
Operator | BSNL
MCC | 404
MNC | 76
APN | bsnlmms

## Slide 3: Operator Information 1
Functionality | Airtel
Website: http://www.airtel.com/ WAP APN: airtelgprs.com | 
Customer care | 199
MNC | 53
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800 – FDD(Band 3)
USSD | To check MDN: *282#
 | Balance check: *123#
 | Data Balance check: *121*114#
VoLTE | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 866
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: http://www.myvi.in WAP APN: www | 
Customer care | 198
MNC | 753
Bands supported | Both FDD and TDD
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN*199#
 | Balance check*121#
 | Data Balance check:*121#
VoLTE | Supported
CSFB | Supported (Switched to 3G)

## Slide 6: Drive Route
Near Cell :- Stationary: RSRP : -65dbm to -75dbm
Cell Edge :- Stationary: RSRP : -95dbm to -110dbm
Mixed :- Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
Near cell(NC) | longitude | latitude | RSRP | PCI | FDD E-ARFCN
1 | 85.757011 | 20.252941 | 74 | 70 | 39294
RSRP:
-65dbm to 75dbm
Kalinga Vihar
Kalinga Vihar LIG, Kalinganagar, Bhubaneswar, Odisha 752054

## Slide 8: Edge Cell (Airtel)
Edge cell(EC) | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.753685 | 20.252340 | 100 | 443 | 39150
RSRP:
-95dbm to -110dbm
Kalinga Vihar
Kalinga Vihar LIG, Kalinganagar, Bhubaneswar, Odisha 752054

## Slide 9
Mixed Mobility(Airtel)
RSRP: -65dbm to -110dbm
Kalinga Vihar LIG, Kalinganagar, Bhubaneswar, Odisha 752054

## Slide 10
Airtel Band HO
Band Hand Over | Longitude | Latitude | RSRP
1 | 85.75308 | 20.2515 | -85 to 105 dBM
Band 3_40
Band 40_3

## Slide 11: Near Cell (Reliance JIO)
Near cell(NC) | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.747753 | 20.240803 | 74 | 277 | 38750
RSRP:
-65dbm to -75dbm
Naragoda
Bhubaneswar, Odisha 752054

## Slide 12
Edge Cell (Reliance JIO)
Edge cell(NC) | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.754094 | 20.241294 | 95 | 94 | 38948
RSRP:
-95dbm to -110dbm
Kalinga Vihar
Kalinga Vihar LIG, Kalinganagar, Bhubaneswar, Odisha 752054

## Slide 13
Mixed Mobility (Reliance JIO)
RSRP: -95dbm to -110dbm

## Slide 14: Reliance JIO Band HO
Band Handover | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.7496 | 20.2385 | 92 | 300 | 38750

## Slide 15: RJIO Band 40 Near Cell:
Near cell

## Slide 16: RJIO Band 40 Edge Cell:
Cell Edge

## Slide 17: Near Cell (VIL)
Near cell(NC) | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.758556 | 20.269859 | 71 | 229 | 1250
Ghatikia Main Rd
Ghatikia, Bhubaneswar, Odisha 751003
RSRP:
-65dbm to -75dbm

## Slide 18: Cell Edge (VI)
Edge cell(EC) | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 85.760398 | 20.265095 | 99 | 271 | 1250
RSRP:
-95dbm to -105dbm
Kalinganagar
Bhubaneswar, Odisha 751003

## Slide 19: Mixed Mobility (VIL)

## Slide 20: VIL Band HO
* In my location only band 3 available for operator VIL

## Slide 21: G net Tracker Drive Route
VIL
Airtel
JIO

## Slide 22: Google Driver Route

## Slide 23
5G Near Cell,Airtel (Bhubaneshwar)
Lat/Long -20°15'38.8"N 85°50'17.1"E
Location-Rajmahal Flyover near The Shivalik hotel Ashok Nagar
Specification –Stable Airtel 5G NSA network
Good Throughput

## Slide 24
NR to LTE Handover ,Airtel (Bhubaneshwar)
Lat. 20.253972, 85.803454to Location –Kala Bhoomi Odisha Crafts Museum/Near Jagamara Specification –Band Handover ,Weak coverage

## Slide 25
NR to LTE Handover ,JIO (Bhubaneshwar)
Lat/Long 20.083104, 85.949672 to
Lat/Long 20.089347, 85.926234 Location – Pipli Konark Road (Dhanua,Bhuan Bridge)
Specification –Band Handover ,Weak coverage

## Slide 26: DRIVE ROUTE Airtel 5G (Bhubaneshwar) Specification-Call/Throughput/Handover/Cell Reselection/Redirection

## Slide 27: DRIVE ROUTE JIO 5G (Bhubaneshwar) Specification-Call/Throughput/Handover/Cell Reselection/Redirection

## Slide 28: DRIVE ROUTE VI 4G (Bhubaneshwar) Specification-Call/Throughput/Handover/Cell Reselection/Redirection

## Slide 29: Airtel 5G SA location-Ashok Nagar lat/long-20.2663890, 85.837549

## Slide 30: Airtel SA Throughput location- RKP variety store near Shiva Nagar lat/long-20.2486586, 85.8346281

## Slide 31: Airtel NSA Throughput location- near bhaina hotel lat/long- 20.1962559970576, 85.85988713515906

## Slide 32: Jio LTE and SA Throughput location- the saffron hotel, ashok nagar lat/long- 20.262036954516592, 85.8398605945562

## Slide 33: Location for 2 CA Throughput for JiO, Airtel,VI Lat / Long-20.262032, 85.83858 Location- Near Hotel Sambit Royale

## Slide 34
JIO 5G Location
Lat/ long 20.276639, 85.862195
Location –Jharapada

## Slide 35: JIO 5G SA to 4G VoLTE handover Ashok Nagar Lat/Long- 20.261114312381487, 85.83839848628462

## Slide 36: Airtel 5G to 4G VoLTE handover Banamalipur road Lat/Long- 20.202291381491747, 85.86243135573218

## Slide 37: THANK YOU
MARQUIS TECHNOLOGIES