## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, VI& Reliance JIO ,BSNL(FDD/TDD) LTE

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 863
APN | Jionet
Operator | Airtel 4G
MCC | 404
MNC | 93
APN | Airtelgprs.com
Operator | VI
MCC | 404
MNC | 78
APN | Internet
Operator | BSNL
MCC | 404
MNC | 58
APN | bsnlnet

## Slide 3: Operator Information 1
Functionality | Airtel
Website: http://www.airtel.com/ WAP APN: airtelgprs.com | 
Customer care | 199
MNC | 93
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800,850 MHz – FDD(Band 3)
USSD | To check MDN: *282#
 | Balance check: *123#
 | Data Balance check: *121*114#
VoLTE | Supported
CSFB | Supported(2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 856
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: https://www.vodafoneidea.com/ WAP APN: www | 
Customer care | 198
MNC | 78
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 41)
 | LTE 850 MHz – FDD(Band 8)
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN*199#
 | Balance check198
 | Data Balance check: 121
VoLTE | Not supported
CSFB | Supported (switched to 2G)

## Slide 6: Drive Route
Near Cell :- Stationary: RSRP : -65dbm to -75dbm
Cell Edge :- Stationary: RSRP : -95dbm to -110dbm
Mixed :- Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
Near cell(NC) | longitude | Latitude | RSRP | Cell id | FDD E-ARFCN
1 | 81.673604 | 21.260236 | -67 | 1 | 1562
RSRP:
-65dbm to 75dbm

## Slide 8: Edge Cell (Airtel)
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 81.681120 | 21.259053 | -101 | 108 | 39150
RSRP:
--115

## Slide 9
Mixed Mobility:- Airtel (Raipur )
RSRP: -60dbm to -110dbm

## Slide 10
Airtel Band HO

## Slide 11: Near Cell (Reliance JIO)
Near cell(NC) | longitude | Latitude | RSRP | Cell id | TDD E-ARFCN
1 | 81.675090 | 21.261822 | 62 | 25 | 38948
RSRP:
-57dbm to -75dbm
SHANKAR NAGAR,
RAIPUR.

## Slide 12
Edge Cell (Reliance JIO)
Edge cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 81.674013 | 21.260036 | -95 | 21 | 38948
RSRP:
-95dbm to -110dbm

## Slide 13
Mixed Mobility:- JI0 RAIPUR
RSRP: -60dbm to -110dbm

## Slide 14: Inter Band Handover (FDD-TDD), JIO 4G

## Slide 15: Near Cell VI:
Near cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 81.673528 | 21.261563 | -66 | 53 | 40140
RSRP:
-65dbm to -75dbm

## Slide 16: Cell Edge VI:
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 81.674663 | 21.259596 | -96 | 32 | 39400
RSRP:
-95dbm to -105dbm

## Slide 17: Mixed coverage area Vodafone:

## Slide 18: Inter Band Handover (FDD-TDD), VI 4G

## Slide 19: Overall Drive Route

## Slide 20: THANK YOU
MARQUIS TECHNOLOGIES