## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, Idea, VODAFONE & Reliance JIO (FDD/TDD) LTE

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 866
APN | jionet
Operator | Airtel 4G
MCC | 405
MNC | 53
APN | airtelgprs.com
Operator | VI
MCC | 405
MNC | 753
APN | www

## Slide 3: Operator Information 1
Functionality | Airtel
Website: http://www.airtel.com/ WAP APN: airtelgprs.com | 
Customer care | 199
MNC | 53
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 2100 MHz - FDD(Band 1)
 | LTE 1800 MHz – FDD(Band 3)
 | LTE 900 MHz – FDD(Band 8)
USSD | To check MDN: *282#
 | Balance check: *123#
 | Data Balance check: *121*114#
VoLTE | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: http://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 866
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: http://www.vodafone.com WAP APN: www | 
Customer care | 198
MNC | 753
Bands supported | Both FDD
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN*199#
 | Balance check198
 | Data Balance check: 121
VoLTE | Supported
CSFB | Supported (CSFB to 3G)

## Slide 6: Drive Route
Near Cell :- Stationary: RSRP : -65dbm to -75dbm
Cell Edge :- Stationary: RSRP : -95dbm to -110dbm
Mixed :- Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
RSRP:
-65dbm to 75dbm
Berhampur - Lochapada Main Rd, Brajanagar, Brahmapur, Odisha 760001

## Slide 8: Near Cell Airtel G-Net Snap
Near cell(NC) | Longitude | latitude | RSRP | Cell id | FDD E-ARFCN
1 | 84.798208 | 19.322258 | 61 | 2 | 1571

## Slide 9: Edge Cell (Airtel)
RSRP:
-95dbm to -110dbm
Berhampur - Lochapada Main Rd, Brajanagar, Brahmapur, Odisha 760001

## Slide 10: Edge Cell Airtel G-Net Snap
Edge cell(EC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 84.797791 | 19.321576 | 102 | 13 | 39348

## Slide 11
Mixed Mobility Airtel:-
Bhakta Salabega Colony
Brahmapur, Odisha 760010
RSRP:
-95dbm TO -110dbm

## Slide 12: Mixed Mobility Airtel G-Net Snap

## Slide 13
Inter Band Handover (FDD-TDD) Airtel
Band Hand Over | Longitude | Latitude | RSRP
1 | 84.794181 | 19.314950 | -85 to 105 dBM

## Slide 14: Near Cell (Reliance JIO)
RSRP:
-65dbm to -75dbm
Brajanagar, Brahmapur, Odisha 760001

## Slide 15: Near Cell Jio G-Net Snap
Near cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 84.802738 | 19.319415 | 67 | 2 | 38948

## Slide 16
Edge Cell (Reliance JIO)
RSRP:
-95dbm to -110dbm
Bapuji Nagar 5th Lane, Medical Bank Colony, Jyoti Nagar, Brahmapur, Odisha 760004

## Slide 17
Edge Cell Jio G-Net Snap
Edge cell(NC) | longitude | latitude | RSRP | Cell id | TDD E-ARFCN
1 | 84.802053 | 19.317626 | 98 | 25 | 38948

## Slide 18
Mixed Mobility Jio:-

## Slide 19
Mixed Mobility Jio G-net Snap

## Slide 20: Inter Band Handover (FDD-TDD) JIO 4G
Band Handover | longitude | latitude | RSRP | PCI | TDD E-ARFCN
1 | 84.777108 | 19.319665 | 90 | 44 | 38948

## Slide 21: RJIO Band 40 Near Cell:-
Lat -19.319560 Long-84.802771

## Slide 22: Near Cell VI:-
2nd Lane number-5, Brajanagar, Berhampur, odisha
RSRP:
-65dbm to -75dbm

## Slide 23: Near Cell VI G-Net Snap
Near cell(NC) | longitude | latitude | RSRP | Cell id | FDD E-ARFCN
1 | 84.798225 | 19.320778 | 67 | 1 | 1250

## Slide 24: Cell Edge VI:-
RSRP:
-95dbm to -105dbm
Bhakta Salabega Colony
Brahmapur, Odisha 760010

## Slide 25: Cell Edge VI G-Net Snap
Edge cell(EC) | longitude | latitude | RSRP | Cell id | FDD E-ARFCN
1 | 84.845136 | 19.30746 | 101 | 2 | 1250

## Slide 26: Mixed Mobility VI:-

## Slide 27: Airtel & VI SRVCC UTRAN
SRVCC Point Not Found

## Slide 28: G-Net Tracker Drive Route

## Slide 29: Berhampur Drive Route

## Slide 30: THANK YOU
MARQUIS TECHNOLOGIES